BYLAW # 2

A SUBDIVISION BYLAW

The council of the Village of Fredericton Junction under the authority vested in it by subsection (1) of section 27 of the Community Planning Act, enacts as follows:

# TITLE

- This bylaw may be cited as the Fredericton Junction Subdivision Bylaw.

## TENTATIVE PLAN

- (1)  A person seeking approval of a subdivision plan shall submit to the com-

mission two copies of a tentative plan, drawn to a scale of one inch to 100 feet,

together with a written application for approval of such tentative plan.

- No fee shall be payable upon application for approval of a tentative plan.

### STREETS

- (1)  Streets in a subdivision shall have a minimum width of 66 feet.

- Courts shall have a maximum length of 600 feet, and shall terminate with a

Circular area having a minimum radius of 50 feet.

- To the satisfaction of the commission, streets shall be

- located with due regard to topography, general traffic requirements, exist-

ing streets in or adjoining the subdivision, and the development of adjacent

properties; and

- laid out so as to intersect as nearly as possible at right angles, and in no

case shall one street intersect another at an angle of less than 60 degrees.

- Where a subdivision abuts on, or includes, an existing or proposed arterial

street, the commission may require streets parallel thereto and such arrangement

of lots, streets and screen planting as it may deem necessary to adequately pro-

tect residential properties from the effects of traffic.

- Reserve strips abutting on a street are prohibited, except where such strips are

vested in the municipality.

- The maximum gradient of streets in a subdivision shall be 8 per cent, except

that the commission may, in exceptional cases made necessary by the topography

of the land in the subdivision, and with the consent of the Provincial Planning

Board, approve a gradient greater than 8 per cent.

- Street names shall be subject to the approval of the commission.

- The commission may require, as a condition of approval of a subdivision plan

of land that, where access will be gained to the subdivision by means of an exist-

ing street, such provision as the commission deems necessary to be made by the

person seeking approval of the subdivision plan to bring the existing street to the

same standard as streets within the subdivision.

### BLOCKS

- (1)  To the satisfaction of the commission, the dimensions and shapes of blocks

shall be determined with due regard to

- the provision of lots suitable for the intended use;

- if a zoning bylaw is in effect, the requirements of such bylaw;

- provision for convenient access, circulation and control of vehicular traffic to ensure the public safety; and

- topography.

- Blocks shall not exceed 800 feet, or be less than 400 feet, in length, and shall

have a minimum width of two lots.

- (1)  Unless otherwise approved by the commission, every lot or other parcel of

land in a subdivision shall abut on a street.

- Every lot intended for residential purposes in a subdivision, in an area serv-

Iced by public water and sewerage facilities, shall have

- a minimum area of 6,000 square feet;

- a minimum frontage of 60 feet; and

- a minimum depth of 100 feet.

- Every lot intended for residential purposes in a subdivision, in an area serv-

iced by either public water or sewerage facilities, but not both, shall have

- a minimum area of 7,500 square feet;

- a minimum frontage of 75 feet; and

- a minimum depth of 100 feet.

- Every lot intended for residentail purposes in a subdivision, in an area not serviced by either public water or sewerage facilities, shall have

- a minimum area of 15,000 square feet;

- a minimum area of frontage of 120 feet; and

- a minimum depth of 125 feet.

- The minimum frontage shall be measured at the line of minimum set-back, as

provided by regulation or by-law, and such minimum width shall be maintained

for a depth of at least 30 feet to the rear of such a line of set-back.

# PEDESTRIAN WALKWAYS

- Pedestrian Walkways, in a width deemed necessary by the commission, shall be

provided when deemed necessary by the commission to provide access or circul-

ation to schools, libraries, playgrounds and other such facilities.

### EASEMENTS

- Easements shall be provided for utilities when necessary, and shall be at least 10

feet wide.

# CONDITIONS OF APPROVAL

- No approval of a subdivision plan shall be given unless, in the opinion of the

Commission,

- the land is suited for the purpose for which the subdivision is intended and

may reasonably be expected to be used for that purpose within a reasonable time

after the subdivision plan is approved;

- the proposed subdivision conforms to the provisions of any by-law in the

municipality; and

- the proposed manner of subdivision will not prejudice the possibility of

further subdividing land in the subdivision, or the convenient subdivision of

adjoining land.

- The secretary of the commission is authorized by the council to enter, at any

reasonable  time, any land or building in the municipality for the purpose of

making and inspection or examination relating to subdivisions, or of adminis-

tering or enforcing this by-law or any provision of the Community Planning Act

relating to subdivisions.

#### Passed this Ninteenth day of September 1967

______Ray Harris______________	______Frank Bean______________

##### Clerk				Mayor